## Slide 1
TECH HORIZON 2.0 · THEME: NEXT-GEN COMMUNICATION
VOID-NAV
An infrastructure-independent SOS network: public SOS nodes and a controlled LoRa relay mesh that carry prioritised, acknowledged emergency messages when towers and internet are down.
PROBLEM STATEMENT
In a major disaster, cellular towers, internet and power fail together. Survivors cannot ask for help, share their location, or reach family, even when responders are only a few kilometres away.
A replacement network must work with no cellular or internet dependency, and it must not collapse under its own traffic: as more survivors transmit, retransmissions, duplicates and simultaneous packets can saturate a low-bandwidth radio channel.
We need controlled forwarding, priority for urgent cases, delivery acknowledgements and location reporting, within LoRa's airtime limits.
Team: Team VOID Team ID: [to be filled] Category: Next-Gen Communication
Members: [Name 1] · [Name 2] · [Name 3] · [Name 4]
Towers down
no cellular, no internet
Shared channel
limited LoRa airtime
Must confirm
sent ≠ delivered
DISASTER ZONE → PUBLIC SOS NODES → RELAYS → RESPONSE
Cell towers · internet · grid: DOWN
Hospital
SOS
Gram panchayat
SOS
Railway station
SOS
Relay 1
Relay 2
Relay 3
Relay 4
SOS receiving station
RX
Emergency ops dashboard
SOS message path
acknowledgement (return)
alternative route
Illustrative layout: actual SOS sites and relay positions are chosen during preparedness planning.
TEAM VOID · VOID-NAV · DISASTER-RESILIENT SOS COMMUNICATION
01 / 06

## Slide 2
02 · VOID-NAV · TECH HORIZON 2.0
Proposed Solution
Public SOS points + structured requests + controlled LoRa relaying + end-to-end acknowledgements
PROBLEM AT HAND
1
Communications fail
Towers, internet and power go down together; phones lose service.
2
No way to ask for help
Survivors can't reliably request rescue, medical aid or supplies.
3
Location is unknown
Families and responders can't tell where a request came from.
4
Forwarding congests
Unchecked rebroadcasts, duplicates and collisions waste scarce LoRa airtime.
OUR SOLUTION · SYSTEM ARCHITECTURE
phone (optional)
SOS ACCESS NODE
1 Rescue now
2 Injured / medical
3 Trapped
4 Food / water
5 Safe, tell family
sent
ack
ESP32 + LoRa + GPS/fixed loc
Relay 1
Relay 2
Relay 3
SOS RECEIVING STATION
decode · verify · ACK
Ops dashboard
map · priority list
1
2
3
4
5
6
message path
ACK return path
alternative route if Relay 2 fails
① survivor reaches node ② picks message, node builds packet ③ relays forward toward station ④ station decodes & ACKs ⑤ dashboard shows request + location ⑥ ACK returns → green LED
Disaster
SOS node
Packet (21 B)
Relay hops
Station
Dashboard
ACK back
Optional path: phone → node Wi-Fi hotspot → local web form → same LoRa packet (custom text ≤ 40 B).
KEY FEATURES
◎
Infrastructure-independent
local radio only; no cellular, internet or cloud
▤
Structured SOS menus
pre-loaded categories, yes/no and counts
⇄
Multi-hop forwarding
relays carry packets beyond one radio link
Wi
Phone-to-node Wi-Fi (opt.)
local web form for short custom text
⌖
Location-linked reports
node GPS or surveyed fixed-node location, labelled
✓
Two-way acknowledgement
orange = sent · green = delivered
▲
Priority, congestion-aware
P0 rescue first; dedup, hop limit, backoff
↻
Store-and-forward
buffer with expiry during link outages
WHY WE STAND OUT
LoRa itself isn't the novelty. The value is the integration: accessible public SOS points + one-touch structured requests that fit in ~21 bytes + a forwarding protocol we implement ourselves (distance-gradient forwarding, duplicate suppression, hop limits, priority queues, bounded retries) + end-to-end acknowledgements that tell a survivor their message actually arrived, with explicit, honest location labels.
TEAM VOID · VOID-NAV · DISASTER-RESILIENT SOS COMMUNICATION
02 / 06

## Slide 3
03 · VOID-NAV · TECH HORIZON 2.0
Technical Approach
How a request is created, carried across a congested shared channel, and confirmed back to the survivor
1
Alert, access & request
PROPOSED ALERT INTEGRATION (NOT CONNECTED)
Disaster declared
Authorised warning*
SOS node map shared
Survivor reaches node
*e.g. via an authorised CAP-based channel such as NDMA SACHET; proposed only
NODE MENU · URGENT FIRST, ≤ 4 PRESSES
1 · CATEGORY
▶ Rescue now (P0)
Injured/medical (P0)
Trapped (P0)
More ▾
2 · INJURED?
▶ Yes
No
3 · PEOPLE
1
▶ 2–5
6+
4 · CONFIRM
Rescue · injured · 2–5
▶ SEND
PACKET BUILT ON NODE · 21 BYTES
T
1
msg_id
4
dst
2
P
1
d
1
a
1
c
1
n
1
f
1
location + label
8
T type · P priority+hops left · d distance-to-station · a age · c category · n people · f flags
Location is labelled: STATION (surveyed coords of a fixed public node) or NODE-GPS (portable node). Not the survivor's exact position. Phone form adds a landmark; browser geolocation needs HTTPS, so it isn't assumed.
2
Controlled message transport
App: menu · queues
VOID-NAV protocol (ours)
RadioLib driver · CAD
SX127x LoRa · 865–867 MHz
① RX packet
② Valid?
CRC (radio) · version · length
drop
③ Seen msg_id?
dedup table: 128 IDs, 15 min
drop
④ Hops left & age < TTL?
hop limit 4 (open decision 3–5)
drop
⑤ Addressed to me?
yes → deliver + ACK · no → ⑥
deliver
⑥ Gradient rule
forward only if my_dist < sender_dist
silent
⑦ Enqueue by priority
P0→P3 · ages +1 class / 60 s · cap 32
evict
⑧ CAD + random backoff
window by priority; cancel if overheard
cancel
⑨ Transmit
hops−1, dist = my_dist, age++
⑩ Await echo / ACK
bounded retry (originator)
 | Priority class | Backoff win. | TTL | Retries
P0 | Rescue · trapped · medical | 0–150 ms | 30 min | 5
P1 | Child/elder · report other | 0–300 ms | 30 min | 4
P2 | Food · water | 0–600 ms | 20 min | 3
P3 | Safe · family (≤ 1 per 30 s/node) | 0–1.2 s | 10 min | 2
3
Destination & confirmation
RX at receiving station
Dedup + decode category, n, flags
Show location + label on map
Rank by priority, alert operator
ACK(msg_id) back to origin
Ops dashboard
P0 · 2–5 · inj.
P0 · 1 · trapped
P1 · elder
P2 · water
loc: STATION #GP-07 (surveyed)
Reverse-path ACK: each relay caches msg_id → previous hop when forwarding; the ACK retraces that path hop by hop. If a hop is gone, the ACK falls back to gradient forwarding (same rules).
ORIGINATING-NODE LED STATES
Sent
TX done ≠ delivered
Retrying
blink · k/5
ACK
msg_id matched
Dispatch
separate msg → screen text
No ACK after final retry → orange off, screen: "Not confirmed. Retry or use next SOS point."
TECHNICAL STACK
Hardware
MVP
ESP32 dev board · SX1276-family LoRa module (865–867 MHz variant) · 128×64 OLED + 4 buttons · orange/green LEDs
Radio config
MVP
LoRa 125 kHz BW · SF9 baseline (SF7–10 to tune) · CR 4/5 · ≈185 ms per 21 B packet (calc.)
Firmware
MVP / opt.
Arduino-ESP32 · RadioLib (CAD) · ESP32 SoftAP + local web form for phones
Messaging layer
MVP core
VOID-NAV protocol: msg_id, dedup, hop/TTL, gradient forwarding, P0–P3 queues, ACK + retries
Location
MVP / prop.
surveyed coords for fixed nodes · GPS module (e.g. NEO-6M) on portable nodes · phone landmark text
Dashboard
MVP
station node → USB serial → local Python web map with cached offline tiles
TEAM VOID · VOID-NAV · DISASTER-RESILIENT SOS COMMUNICATION
03 / 06

## Slide 4
04 · VOID-NAV · TECH HORIZON 2.0
Feasibility, Viability & Risk Mitigation
Built incrementally on commodity ESP32 + LoRa hardware, with every risky assumption named and testable
A
Why the system is feasible
✓
ESP32 controller
dual-core MCU with built-in Wi-Fi; mature Arduino/ESP-IDF toolchains
✓
LoRa modules available
SX127x-family modules with 865–867 MHz variants are sold in India
✓
Local Wi-Fi interface
ESP32 SoftAP + small web server serves a form with no internet
✓
Small structured payloads
21 B request ≈ 185 ms airtime at SF9/125 kHz (formula-based)
✓
Incremental build
each layer (link → relay → ACK → priority) testable on its own
✓
No cloud, no cellular
the LoRa path is fully local; the dashboard runs on a laptop
B
How we build it
1
Point-to-point LoRa link
exit: stable RX/TX, RSSI logged
2
Packet format + unique msg_id
exit: 21 B frames decode at station
3
Relay forwarding + dedup + hop limit
exit: 3-hop chain, no duplicate storms
4
Menu UI + LED states
exit: request in ≤ 4 presses
5
ACK return path, retries, priority queues + CAD backoff
exit: green LED on matched ACK
6
Location + dashboard; load & failure tests
exit: metrics from slide 5 plan
C
Risks & mitigation
Risk | Effect | Mitigation
Simultaneous TX / collisions | lost packets; retries add load | CAD before TX, priority-scaled random backoff, cancel if overheard; collisions reduced, never eliminated
Relay congestion | queues fill, latency grows | gradient forwarding (not blind flooding), P3 rate limit, queue cap 32 with lowest-priority eviction
Lost ACKs → repeats | duplicate traffic | retries reuse msg_id → relays drop dups; station re-ACKs without re-alerting; capped retries
Relay or station offline | route breaks | another lower-distance relay forwards; store-and-forward until TTL; distance beacons refresh
Wrong / missing location | help sent to wrong place | explicit label: STATION / NODE-GPS / NONE; surveyed coords at install; GPS fix age
Limited bandwidth & payload | text crowds out urgent traffic | 21 B structured frames; custom text ≤ 40 B, single frame, no fragmentation in MVP
Forged / spam messages | false alarms, wasted airtime | node-ID allow-list + rate limits (MVP); message authentication with a network key (proposed)
Power failure at SOS site | node offline | battery + solar enclosure (proposed); relay sleep; battery level in beacons
Radio regulation | non-compliance | stay in 865–867 MHz exempt band, 125 kHz BW (< 200 kHz); verify power limits in GSR 853(E)
D
Prototype vs deployment
Capability | Hackathon PoC | Deployment
LoRa P2P + 3-hop relay | planned demo | field test
Dedup, hop limit, gradient rule | planned demo | tune at scale
Priority queues + CAD backoff | planned demo | load test
End-to-end ACK + LEDs | planned demo | field test
Phone Wi-Fi form | optional | optional
Fixed / GPS location label | planned demo | survey all sites
Ops dashboard (offline) | planned demo | multi-station
Solar enclosure, auth key | — | proposed
Public-warning integration | — | proposed, needs partner
Status: "planned demo" = target for our hackathon build, [confirm before submission]. Nothing above is claimed as already tested.
BOM template: ESP32 · LoRa module + antenna · OLED + 4 buttons · 2 LEDs · GPS (portable) · battery/solar · enclosure → unit costs [fill from supplier quotes].
TEAM VOID · VOID-NAV · DISASTER-RESILIENT SOS COMMUNICATION
04 / 06

## Slide 5
05 · VOID-NAV · TECH HORIZON 2.0
Impact & Benefits
Keeping a usable emergency pathway open when conventional infrastructure is gone
◉
Survivors without signal
can request help from a nearby public SOS point
✚
Urgent medical / rescue
P0 requests get first use of scarce airtime
♥
Families
"I am safe" messages travel when calls cannot
◎
Authorities
one prioritised, location-labelled list of requests
⌂
Public facilities
hospitals, panchayats, stations become comms points
CAPABILITY → OPERATIONAL BENEFIT → INTENDED OUTCOME
Capability
Operational benefit
Intended outcome
Pre-loaded structured messages
request in a few presses, no typing
help asked for even under stress
Multi-hop relays
reach beyond one radio link
coverage across the affected area*
Labelled location data
responder knows which site sent it
teams go to the right place
End-to-end acknowledgements
survivor sees green when delivered
less panic-driven resending
Priority handling
airtime goes to urgent cases first
critical requests surface first
Store-and-forward + controlled relaying
survives short link outages
messages arrive late rather than never
*subject to radio range, terrain, relay placement and channel capacity, which must be measured on site.
CAPACITY & LATENCY (ESTIMATES)
More relays ≠ more capacity. Nodes in radio range share one channel. One P0 request over 3 hops plus its ACK uses ≈ 3×185 + 3×144 ≈ 1.0 s of airtime, so at a cautious 20–30 % channel load one shared channel carries roughly 12–18 such requests per minute. Scaling means more receiving stations and separate areas, not just more relays.
Per hop, P0 (SF9, 21 B) | ms
CAD check (~2 symbols) | ≈ 8
Random backoff (avg of 0–150) | ≈ 75
Time on air | ≈ 185
Processing / queue | ≈ 10
3 hops forward | ≈ 0.85 s
ACK back, 3 hops (10 B) | ≈ 0.7 s
Round trip, idle channel | ≈ 1.6 s
Proposed targets (to measure): P0 ACK ≤ 5 s at 3 hops · delivery ratio ≥ 95 % at test load · transmissions per delivered request ≤ hops + 2 · reported at 1, 5, 20 requests/min and with one relay removed.
Intended outcome: when towers and internet are gone, survivors still have a nearby place to ask for help, and responders still receive a prioritised, location-labelled list of who needs it.
TEAM VOID · VOID-NAV · DISASTER-RESILIENT SOS COMMUNICATION
05 / 06

## Slide 6
06 · VOID-NAV · TECH HORIZON 2.0
Research & References
What published work establishes, how it shapes VOID-NAV, and what we still have to prove
Area | Established technique / finding (click to open) | How it informs our design | Status
LoRa airtime | Semtech AN1200.13, LoRa Modem Designer's Guide: time-on-air formula; airtime rises with SF and payload ↗ link | 21 B structured frame; SF9 baseline ≈185 ms; custom text capped at 40 B | Design basis
LoRa scalability | Bor, Roedig, Voigt, Alonso. "Do LoRa Low-Power Wide-Area Networks Scale?" ACM MSWiM 2016: collisions limit density; parameter choice and multiple sinks help ↗ link | short frames, priority backoff, plan for several receiving stations | Needs evaluation
Managed flooding | Meshtastic, Mesh Broadcast Algorithm: hop-limited flooding, listen-before-rebroadcast, SNR-based contention window ↗ link | dedup, hop limit, cancel-if-overheard; we add a distance-gradient rule and priority classes | MVP core
Why flood routing | Meshtastic blog, "Why Meshtastic uses managed flood routing": trade-offs of flooding vs routed meshes ↗ link | keep routing simple; limit flood scope with gradient + hop limit | MVP core
Channel activity detection | Semtech, "Channel Activity Detection: ensuring your LoRa packets are sent": CAD detects LoRa preambles/chirps, not full carrier sense ↗ link | CAD + random backoff before TX; collisions still possible | MVP (to test)
SX1276 radio | Semtech SX1276/77/78/79 datasheet: LoRa modem, CAD mode, programmable SF/BW/CR ↗ link | radio settings and CAD use match the actual chip | Design basis
ESP32 SoftAP | Espressif ESP-IDF Wi-Fi API (AP/STA modes); SoftAP example: max_connection default 4 ↗ link | optional phone form; few phones per node at a time | Optional
Browser location | MDN Geolocation API & Chrome: geolocation only in secure contexts (HTTPS) ↗ link | don't assume phone GPS on a local HTTP portal; use labelled node location | Design constraint
Indian band rules | DoT clarification on 865–867 MHz (1 W TX, 4 W ERP, 200 kHz carrier); GSR 853(E) 2021, 865–868 MHz SRD exemption rules ↗ link | 125 kHz BW inside 200 kHz; verify current limits in the 2021 gazette text | Must verify
Regional plan | LoRa Alliance RP002-1.0.3 Regional Parameters, IN865-867 section ↗ link | channel-plan reference (we do not run LoRaWAN) | Reference
Public warning | NDMA CAP-based Integrated Alert System (SACHET), built with C-DOT ↗ link | proposed route to announce SOS node locations; no integration exists | Proposed
Read this right: published work supports individual techniques (airtime, CAD, managed flooding, band rules). It does not show that VOID-NAV as a whole works. Our own contribution is the integration and protocol design, and every performance figure in this deck is an estimate or target until measured on our prototype.
TEAM VOID · VOID-NAV · DISASTER-RESILIENT SOS COMMUNICATION
06 / 06