## Slide 1
QUANTUM PNT FOR DRONES
PLUS QISKIT FALL FEST 2026
01
UC-085 · DEFENCE & STRATEGIC APPLICATIONS
VOID-NAV
Navigating without the sky: a quantum-assisted positioning payload that reads the Earth's magnetic fingerprint when GNSS is jammed, spoofed or unavailable.
Quantum sensing
Grover search
Quantum kernel ML
QAOA planning
TEAM
Team VOID
DELIVERABLE
Working payload prototype + Qiskit pipeline + live dashboard
VIDEO PITCH
https://youtu.be/BV2KYV-yhL0

## Slide 2
PROBLEM STATEMENT
PLUS QISKIT FALL FEST 2026
02
Without GNSS, a drone's inertial position drifts without bound.
10⁻¹⁶ W
GNSS power at the receiver: weaker than background noise, easily denied by jamming, terrain, tunnels or foliage.
~260 m
Mean error after 3 min of MEMS-only dead reckoning in our drift model: error grows with t², not t.
₹10L+
Cost of navigation-grade INS or cold-atom units: too expensive to fit on every tactical drone.
Chart: Position error after GPS loss (m), simulated
| 0s | 10s | 20s | 30s | 40s | 50s | 60s | 70s | 80s | 90s | 100s | 110s | 120s | 130s | 140s | 150s | 160s | 170s
Inertial only (MEMS IMU) | 0 | 1.1 | 3.7 | 7.8 | 13.6 | 20.9 | 29.9 | 40.5 | 52.6 | 66.3 | 81.6 | 98.5 | 117 | 137.1 | 158.8 | 182 | 206.9 | 233.5
VOID-NAV (MEMS mag fix) | 0 | 5.6 | 5.5 | 5.4 | 5.6 | 5.4 | 5.6 | 5.2 | 4.9 | 4.8 | 5.3 | 5.3 | 5.1 | 5.4 | 5.3 | 5.1 | 5.8 | 5.6
Problem: give a defence UAV a position it can trust within metres when GNSS disappears, with a passive (non-emitting), low-cost payload that is ready to take a quantum magnetometer, as UC-085 and the iDEX passive quantum positioning challenge call for.

## Slide 3
PROPOSED SOLUTION
PLUS QISKIT FALL FEST 2026
03
VOID-NAV: a passive quantum PNT payload. The drone carries it; the payload does the navigation.
1
Map
GPS on: fly or walk the area once and log a 5-D magnetic fingerprint [Bx, By, Bz, |B|, ∇B] per 2 m cell.
2
Sense
GPS off: the magnetometer, IMU, optical flow and barometer track motion; the magnetic field is read as a short window.
3
Match
Quantum engine: Grover's search finds candidate cells, the quantum kernel SVM confirms the zone.
4
Correct
A particle filter fuses the match with dead reckoning, resets IMU drift and sends position + confidence to the autopilot.

## Slide 4
INNOVATION & UNIQUENESS
PLUS QISKIT FALL FEST 2026
04
Most entries show one quantum algorithm. VOID-NAV runs a complete quantum PNT pipeline.
01 · FULL STACK
Sense, search, learn, plan
Quantum sensing, Grover's search, quantum-kernel ML and QAOA each do a distinct job in one navigation loop.
02 · RICHER FINGERPRINT
5-D magnetic gradient map
We match the spatial pattern [Bx, By, Bz, |B|, ∇B], not a single field value, which cuts false matches sharply.
03 · QUANTUM CROSS-CHECK
Grover proposes, QSVM decides
In our run Grover returned two look-alike cells (0110, 1011); the QSVM zone label resolved the tie.
04 · QUANTUM-SENSOR READY
Drop-in NV-diamond slot
Same data interface as an NV magnetometer; we simulate its Ramsey readout today to quantify the upgrade.
05 · MAGNETICALLY AWARE ROUTES
QAOA path planning
Chooses waypoints through magnetically rich cells so the drone gets more position fixes per minute.
06 · DEPLOYABLE
Passive, retrofit, low cost
Emits nothing, speaks MAVLink to any ArduPilot/PX4 drone, prototype under ₹8,000 in parts.
SENSE
Ramsey + IPE
SEARCH
Grover
LEARN
QSVM
PLAN
QAOA
FUSE
Particle filter

## Slide 5
QUANTUM COMPUTING APPROACH
PLUS QISKIT FALL FEST 2026
05
Four quantum building blocks, each mapped to one navigation job.
Q1 · QUANTUM SENSING
Ramsey interferometry + iterative phase estimation
Qubit in superposition via H; field B imprints phase φ = γBτ (γ ≈ 28 GHz/T); phase kickback + IPE reads φ bit by bit. Models an NV-diamond readout.
Q2 · SEARCH
Grover's algorithm · 4 qubits, 16 map cells
Oracle U_f phase-flips cells whose fingerprint matches; diffuser 2|s⟩⟨s|−I amplifies them. ~√N queries; 2 iterations here.
Q3 · LEARNING
Quantum-kernel SVM · ZZ feature map
x ↦ |φ(x)⟩ in a 16-dim Hilbert space; kernel K(x,x′)=|⟨φ(x)|φ(x′)⟩|² feeds a classical SVM (QSVC) to label the zone.
Q4 · PLANNING
QAOA · p = 1, route graph
Cost Hamiltonian H_C = Σ wᵢⱼZᵢZⱼ rewards magnetically rich waypoints; mixer H_M = ΣXᵢ; γ, β tuned by COBYLA.

## Slide 6
QISKIT & TECHNOLOGY STACK
PLUS QISKIT FALL FEST 2026
06
Open-source software on borrowed hardware: built for a student budget.
QUANTUM
Qiskit 2.x SDK · Qiskit Aer · IBM Runtime SamplerV2 · qiskit-machine-learning (FidelityQuantumKernel, QSVC) · QAOA + COBYLA
NAVIGATION
Python · NumPy / SciPy · FilterPy particle filter + EKF · hard/soft-iron calibration
FLIGHT
ArduPilot SITL · pymavlink · MAVLink VISION_POSITION_ESTIMATE / GPS_INPUT
FIRMWARE
ESP32 · Arduino C++ · I²C sensor drivers · 50 Hz UDP stream
INTERFACE
Streamlit + Plotly live map · circuit + histogram panels · CSV / Parquet logs
Part | Role | Source | ₹
QMC5883L magnetometer | Main field sensor (mast) | Buy | 300
MPU-9250 IMU | Accel + gyro | Borrow | 600
BMP280 barometer | Altitude | Borrow | 150
NEO-6M GPS | Mapping + ground truth | Borrow | 450
PMW3901 optical flow | Ground motion | Buy (opt.) | 2,000
ESP32 DevKit | Sensor hub | Borrow | 450
Quadcopter frame / drone | Platform | Borrow | 0
Total if bought |  |  | ≈ 3,950

## Slide 7
SYSTEM ARCHITECTURE / WORKFLOW
PLUS QISKIT FALL FEST 2026
07
Sensors in, trusted position out: quantum where it adds value, classical where speed matters.
SENSE · 50 HZ
Magnetometer
quantum-ready
IMU
accel · gyro
Optical flow
ground motion
Barometer
altitude
GPS
mapping only
PRE-PROCESS
Calibrate
hard/soft iron, tilt
Fingerprint
[Bx,By,Bz,|B|,∇B]
Dead reckoning
IMU + flow → Δx, Δy
QUANTUM ENGINE · QISKIT
Q1 Ramsey / IPE
read field (NV sim)
Q2 Grover
candidate cells
Q3 QSVM
zone label
Q4 QAOA
next waypoints
FUSE & ACT
Particle filter
500 particles; re-weighted only when Grover and QSVM agree
Autopilot
MAVLink position + covariance
Dashboard
map, error, circuits
Loop: classical fusion runs every 20 ms; quantum matching runs every 1 s on a window of readings, so quantum latency never blocks flight control.

## Slide 8
IMPLEMENTATION & FEASIBILITY
PLUS QISKIT FALL FEST 2026
08
Built in 24 hours, with a working fallback at every level.
24-HOUR BUILD PLAN
H0
H4
H8
H12
H16
H20
H24
Hardware
Wire sensors + ESP32 firmware
Calibrate + mapping run
Mount on drone, test
Quantum
Grover + IPE circuits (Aer)
QSVM on map data
QAOA + IBM run
Nav + UI
Dead reckoning + particle filter
Integrate quantum → filter
Dashboard
Rehearse
record backup video
Level 1 · guaranteed
Payload carried along the mapped corridor; live dashboard shows drift vs correction.
Level 2 · main demo
Payload mounted on a borrowed drone, carried or tethered; full flight replayed in ArduPilot SITL on our real map.
Level 3 · bonus
Short real flight with GPS disabled in software, only if a flight-ready drone and venue permission exist.

## Slide 9
EXPECTED RESULTS & IMPACT
PLUS QISKIT FALL FEST 2026
09
Early results from our own Qiskit runs and navigation simulation.
Chart: Grover on Aer · 4,096 shots
| 0000 | 0001 | 0010 | 0011 | 0100 | 0101 | 0110 | 0111 | 1000 | 1001 | 1010 | 1011 | 1100 | 1101 | 1110 | 1111
Shots | 12 | 22 | 15 | 16 | 18 | 9 | 1914 | 20 | 20 | 21 | 22 | 1937 | 13 | 12 | 21 | 24
0110 + 1011 = 94% of shots. Grover returns 2 look-alike cells; QSVM breaks the tie.
Chart: Error after GPS loss (m, log scale)
| 0s | 10s | 20s | 30s | 40s | 50s | 60s | 70s | 80s | 90s | 100s | 110s | 120s | 130s | 140s | 150s | 160s | 170s
Inertial only | 0 | 1.1 | 3.7 | 7.8 | 13.6 | 20.9 | 29.9 | 40.5 | 52.6 | 66.3 | 81.6 | 98.5 | 117 | 137.1 | 158.8 | 182 | 206.9 | 233.5
VOID-NAV · MEMS magnetometer | 0 | 5.6 | 5.5 | 5.4 | 5.6 | 5.4 | 5.6 | 5.2 | 4.9 | 4.8 | 5.3 | 5.3 | 5.1 | 5.4 | 5.3 | 5.1 | 5.8 | 5.6
VOID-NAV · simulated NV sensor | 0 | 0.9 | 0.9 | 0.9 | 0.9 | 0.9 | 0.8 | 0.9 | 0.9 | 0.9 | 0.9 | 0.9 | 0.9 | 0.8 | 0.9 | 1 | 0.9 | 0.9
Quantum kernel matrix. Same-zone fingerprints overlap ~2.8× more than cross-zone ones (0.24 vs 0.09).
~50×
lower drift vs inertial-only (MEMS model)
~6×
further gain with a quantum (NV) magnetometer
0 W
radio emission: fully passive

## Slide 10
FUTURE SCOPE & CONCLUSION
PLUS QISKIT FALL FEST 2026
10
From a hackathon payload to a field-ready quantum PNT module.
NOW · TRL 3
Hackathon
Payload prototype, 16-cell map, 4 quantum blocks on Aer + one IBM hardware run, live dashboard.
6 MONTHS · TRL 4
Scale the map
Campus and outdoor anomaly maps (NGRI / EMAG2), larger Grover circuits, tethered drone trials.
18 MONTHS · TRL 5
Quantum sensor
Swap in an NV-diamond magnetometer with an NQM sensing-hub partner; quantum IMU fusion.
36 MONTHS · TRL 6
Defence trials
Ruggedised module with DRDO / iDEX partners on UAVs, loitering systems and vehicles.
"When GPS goes dark, the ground still knows where you are."
VOID-NAV: quantum sensing, quantum search, quantum learning and quantum planning, flying on one passive payload.
Team VOID
Video: https://youtu.be/BV2KYV-yhL0
THANK YOU · QUESTIONS WELCOME